## Slide 1: Reducing redundancy of vehicle trajectory data for the safety monitoring system of CAVs
What is the problem?
  Fixed sampling rate produces redundant samples for safety monitoring system
  High resolution raw data causes unnecessary V2X communication cost
  Reducing sampling rate causes delay in critical-event detection
Why is this problem important?
  Reducing the cost of the vehicle trajectory collection is key factor for expanding safety monitoring system
  Most of trajectory samples were not useful in safety monitoring system (e.g., excess zeros)
  Self-adaptive sampling (SAS) method can reject redundant data containing the same safety-related information with previous samples
  Previous studies on SAS method barely untouched for safety monitoring system
How can we solve this problem?
  Proposed SAS aims to sample data extensively only when safety-related issue arise
  This study defines sample redundancy with transient probability of risk’s state. (e.g., 5 level).
  Proposed SAS rejects samples with low transient probability of risk
  Long constant sampling interval below the rejection criteria – it can provide macroscopic information.
What is key contribution?
  Proposed SAS reduces communication cost of safety monitoring system by rejecting redundant samples
  Proposed SAS guarantees minimum-delay of critical events detection
  Reconstructed data by the proposed SAS can be utilized for macroscopic information
Rejected sample
Accepted sample
Raw data
Reconstructed data
Transient prob.
Candidate samples
Time
v
(speed)
Time
1
Risk
Rejection criteria
Proposed method
a
(accel.)
Transient
prob
State 4
State 3
State 2
State 1
Safety monitoring system
CAVs